R97 Composite Termination Modules

Description

The common termination system consists of a system of wires and components that interconnected to one another by the use of standard MIL-C-39029/22 socket contact only. This eliminates the need for pin contacts which are located in the mating components. There are approximately twenty different devices that comprise the common termination system. These devices consist of modules, junction, connectors and rail assemblies.

The composite termination module is in accordance with MIL-T-81714 series II and is a new termination component used in the electrical system of wire and components that are interconnected to one another. The modules can be used in design and manufacture, especially in the project development phase. Using the module make the design modification work more easier

Comparing to traditional standard termination structure, the composite termination system reduces weight and enhances performance. The simple system design and high density layout reduces the length of the component and wire, thus reducing the weight. At the same, the composite is lighter than traditional material. Due to the light weight, the module is vibration resistance to ensure the integrity of the wire and connector

The standardization of termination for all systems components simplifies training, saves assembly time, cuts production cost and enhances performance.

Module type

The common termination system consists of s series sealed termination module. The modules are imbedded in the composite rail, including:

[Distribution modules]

Used when two or more contact size are needed per module. The bus bars are also forged from a single copper piece.

[Feedback modules]

Act like a terminal strip. Each module accommodates a single contact size which is bussed internally to a copper bar

[Electronic module]

Designed to contain a variety of circuit arrangements for rectifying, filtering and arc suppression.

[Grounding modules]

Developed to provide multiple grounds made at a common point.

[Grounding junctions]

Provide a simple method of terminating a wire to ground. Wires with crimp contacts are inserted into the grounding junction and can be attached to any conductive surface

[In –line junction]

Used to join two wires. Similar to an in-line splice, but removal

R97D1 Series Distribution Module and R97J1 Series Feedback Module

Description

In accordance with MIL-T-81714 series II The composite termination module uses a rugged socket contact terminated to internal pin-buss bars R97D1 series module accents a large input current and distributes it through a pin-buss system to smaller feeder terminal strips R97J1 series module accommodates common bussing of 6 to 20 contacts in a small area. Internal bussbars are configured to allow connections of various combination of wires providing environmental resistance and vibration dampening Enterprise standard：Q/21EJ501

Main technical characteristic

[Mechanical]

- Random vibration：50～2000Hz，power spectral density 1.0G2/ Hz

- Shock：Acceleration 2940m/s2

[Environmental]

- Operating temperature：-65℃～+200℃

- High temperature durability：200℃，1000h

- Salt spray：500h

- Magnetic permeability：≤2.0

- Fluid immersion：fuels, coolant, solvent

[Electrical]

- Insulation resistance：normal≥5000MΩ  damp & heat≥100MΩ

- Contact resistance and rated current：

| No. | Contact size | Wire size （AWG） | Rated current A | Pull force N | Crimped resistance mΩ | The maximum pressure drop mV |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Before test 25±3℃ | After test |
|  |  |  |  |  |  |  | 25±3℃ | 200℃ |
| 1 | 22# | 22 | 5 | 54 | 1.0 | 70 | 80 | 120 |
|  |  | 26 | 2 | 23 | 2.0 | 60 | 70 | 100 |
| 2 | 20# | 20 | 7.5 | 89 | 0.8 | 55 | 65 | 95 |
|  |  | 24 | 3.0 | 36 | 1.3 | 45 | 55 | 80 |
| 3 | 16# | 16 | 13 | 223 | 0.4 | 50 | 60 | 85 |
|  |  | 18 | 7.5 | 172 | 0.5 | 45 | 55 | 80 |
|  |  | 20 | 7.5 | 89 | 0.7 |  |  |  |
| 4 | 12# | 12 | 23 | 490 | 0.2 | 60 | 70 | 100 |
|  |  | 14 | 17 | 312 | 0.3 | 55 | 65 | 95 |
| 5 | 10# | 10 | 40 | 601 | 0.2 | 40 | 60 | 90 |

- Withstanding voltage：

| No. | Condition | Test voltage V（50Hz，AC RMS） |
| --- | --- | --- |
| 1 | Sea level | 1500 |
| 2 | 15240m | 800 |
| 3 | 21336m | 600 |
| 4 | 30480m | 200 |

How to order

| [R97D1series distribution module] Basic series R97D1 26 E 01A Feedback distribution buss bars See arrangements Environmental E Bussing arrangements See arrangements | [R97J1 series feedback module] Basic series R97J1 20 E 01B Contact size 22、20、16、12、10 Environmental E Bussing arrangements See arrangements |
| --- | --- |

Bussing arrangements

[R97D1 series distribution module bussing arrangements]

[R97J1 series feedback module bussing arrangements]

Outline dimensions

[R97D1 series distribution module]

| P/N | Contact quantity & size | A1） | B | C Max. |
| --- | --- | --- | --- | --- |
| R97D126E01A | 2 size 12、6 size 16 | 25.9 | 17.06 | 24 |
| R97D160E01F | 2 size 16 、6 size 20 | 12.9 | 17.06 | 23 |
| R97D126E02E | 2 size 12 、6 size 16 | 25.9 | 17.06 | 24 |
| R97D1062E05A | 5 size 16 、20 & 22 | 25.9 | 17.06 | 23 |

Note：1）A=12.9mm is for module with single width，A=25.9mm is module wit dual width

[R97J1 series feedback module]

| Contact size | A1） | B | C Max. |
| --- | --- | --- | --- |
| 22 # | 12.9 | 17.06 | 19.3 |
| 20 # | 12.9 | 17.06 | 23 |
| 16 # | 12.9 | 17.06 | 23 |
| 12 # | 25.9 | 17.06 | 24 |

Notes：1）A=12.9mm is for module with single width，A=25.9mm is module wit dual width

R97J4 Series Electronic Module

Description

| Each electronic component module houses small printed circuit boards incorporating diodes, resistors, capacitors, relays, fuses etc. The input/output wiring is sealed with a silicone rubber grommet. This packaging technique allows designer to include circuits in a system that would be considered environmentally hazardous. For example, transient suppression devices can be placed in or near the system or harness they were designed to protect. Other applications including rectifying, filtering, voltage clamping and arc-suppression. Enterprise standard：Q/21EJ501 |  |
| --- | --- |

Main technical characteristic

- Insulation resistance：normal≥5000MΩ；damp & heat≥≥100MΩ

- Rated current 1）：≤7.5A（20#）；≤23A（12#）

- Withstanding voltage：Sea level 1500V；30480m 200V（50Hz，AC RMS）

- Operating temperature 2）：-65℃～+200℃

Note：1）The value is for rated current of contact. Please consider the rated current of the internal electronic component during the actual usage；

2）Refer to the temperature of component

How to order

| Basic series | R97J4 | 20 | E | 002 |
| --- | --- | --- | --- | --- |
| Contact size | 12、20 |  |  |
| Environmental | E |  |  |
| Individual circuit | See specific layout |

Outline dimensions

Typical internal circuit diagrams

* See the following table for resistance and other parameters for diode

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

* See the following table for resistance and other parameters for diode.

[Resistance parameters]

[Parameters for diode]

R97J7 Series Grounding Module

Description

| The grounding module provides an excellent method of grounding multiple wires to a common location. It accepts M39029/22 crimp type sockets that mate with internal pins on a rugged buss bar contained in a sealed plastic housing. The one-piece construction is small, light-weight, dissipates heat, is shock and vibration resistant and has an extremely low voltage drop Enterprise standard：Q/21EJ501 |  |
| --- | --- |

Main technical characteristic

[Mechanical]

- Random vibration：50～2000Hz，power spectral density 1.0G2/ Hz

- Shock：Acceleration 2940m/s2

[Environmental]

- Operating temperature：-65℃～+200℃

- High temperature durability：200℃，1000h

- Salt spray：48h

- Magnetic permeability：≤2.0

- Fluid immersion：fuels, coolant, solvent

[Electrical]

- Insulation resistance：normal≥5000MΩ  damp & heat ≥100MΩ

- Contact resistance and rated current：

| No. | Contact size | Wire size （AWG） | Rated current A | Pull force N | Crimped resistance mΩ | The maximum pressure drop mV |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Before test 25±3℃ | After test |
|  |  |  |  |  |  |  | 25±3℃ | 200℃ |
| 1 | 22# | 22 | 5 | 54 | 1.0 | 70 | 80 | 120 |
|  |  | 26 | 2 | 23 | 2.0 | 60 | 70 | 100 |
| 2 | 20# | 20 | 7.5 | 89 | 0.8 | 55 | 65 | 95 |
|  |  | 24 | 3.0 | 36 | 1.3 | 45 | 55 | 80 |
| 3 | 16# | 16 | 13 | 223 | 0.4 | 50 | 60 | 85 |
|  |  | 18 | 7.5 | 172 | 0.5 | 45 | 55 | 80 |
|  |  | 20 | 7.5 | 89 | 0.7 |  |  |  |
| 4 | 12# | 12 | 23 | 490 | 0.2 | 60 | 70 | 100 |
|  |  | 14 | 17 | 312 | 0.3 | 55 | 65 | 95 |

- Withstanding voltage：Sea level 1500V；30480m 200V（50Hz，AC RMS）

How to order

| Basic series | R97J7 | 22 | K | 01C |
| --- | --- | --- | --- | --- |
| Contact size | 22、20、16、12 |  |  |
| Mounting style | K－Flange mounted E－Stud mounted（Not applicable to 12# contact） |  |  |
| Buss arrangement | See R97J7 series buss arrangement |

R97J7 Series Buss Arrangement

Outline dimensions

[Type K flange mounted（12# contacts）]

|  | P/N Contact size R97J712K01E 12 |
| --- | --- |

[Type K flange mounted（16#、20# and 22# contacts）]

|  | P/N Contact size J R97J722K01C 22 21.0 R97J720K01B 20 24.2 R97J716K01D 16 24.2 |
| --- | --- |

[ Type E stud mounted（16#、20# and 22# contacts）]

|  | P/N Contact size C R97J722E01C 22 21.2 R97J720E01B 20 25.3 R97J716E01D 16 25.3 |
| --- | --- |

During mounting the grounding modules, the contact section between aircraft skin or equipment shell and the bottom of the module should be polished with removing the scale to ensure the reliable contact.

R97G Series Grounding Junction

Description For grounding single wires, a threaded mounting junction is adapted and crimped socket is used on the mating face

Main technical characteristic

[Mechanical]

- Random vibration：50～2000Hz，power spectral density 1.0G2/ Hz

- Shock：Acceleration 2940m/s2

[Environmental]

- Operating temperature：-65℃～+200℃

- High temperature durability：200℃，1000h

- Salt spray：48h

- Magnetic permeability：≤2.0

- Fluid immersion：fuels, coolant, solvent

[Electrical]

- Insulation resistance：normal≥5000MΩ  damp & heat≥100MΩ

- Contact resistance and rated current：

| No. | Contact size | Wire size （AWG） | Rated current A | Pull force N | Crimped resistance mΩ | The maximum pressure drop mV |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Before test 25±3℃ | 试验后 |
|  |  |  |  |  |  |  | 25±3℃ | 200℃ |
| 1 | 22# | 22 | 5 | 54 | 1.0 | 70 | 80 | 120 |
|  |  | 26 | 2 | 23 | 2.0 | 60 | 70 | 100 |
| 2 | 20# | 20 | 7.5 | 89 | 0.8 | 55 | 65 | 95 |
|  |  | 24 | 3.0 | 36 | 1.3 | 45 | 55 | 80 |
| 3 | 16# | 16 | 13 | 223 | 0.4 | 50 | 60 | 85 |
|  |  | 18 | 7.5 | 172 | 0.5 | 45 | 55 | 80 |
|  |  | 20 | 7.5 | 89 | 0.7 |  |  |  |
| 4 | 12# | 12 | 23 | 490 | 0.2 | 60 | 70 | 100 |
|  |  | 14 | 17 | 312 | 0.3 | 55 | 65 | 95 |

- Withstanding voltage：Sea level 1500V；30480m 200V（50Hz，AC RMS）

How to order

| Basic series | R97G | - | 22 |
| --- | --- | --- | --- |
| Dash | － |  |
| Contact size | 22、20、16、12 |  |

Outline dimensions

| P/N | Contact size | A±0.78 | B±0.38 |
| --- | --- | --- | --- |
| R97G-22 | 22 | 33.3 | 4.78 |
| R97G-20 | 20 | 31.5 | 4.78 |
| R97G-16 | 16 | 31.6 | 6.35 |
| R97G-12 | 12 | 34.8 | 7.95 |

R97L Series In-Line Junction

Description

- It is used to connect two wires in-line utilizing crimp-type contacts. The junction can then be placed in a wire bundle without being mounted.

Main technical characteristic

[Mechanical]

- Random vibration：50～2000Hz，power spectral density 1.0G2/ Hz

- Shock：Acceleration 2940m/s2

[Environmental]

- Operating temperature：-65℃～+200℃

- High temperature durability：200℃，1000h

- Salt spray：48h

- Magnetic permeability：≤2.0

- Fluid immersion：fuels, coolant, solvent

[Electrical]

- Insulation resistance：normal≥5000MΩ

- Contact resistance and rated current：

| No. | Contact size | Wire size （AWG） | Rated current A | Pull force N | Crimped resistance mΩ | The maximum pressure drop mV |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Before test 25±3℃ | After test |
|  |  |  |  |  |  |  | 25±3℃ | 200℃ |
| 1 | 22# | 22 | 5 | 54 | 1.0 | 70 | 80 | 120 |
|  |  | 26 | 2 | 23 | 2.0 | 60 | 70 | 100 |
| 2 | 20# | 20 | 7.5 | 89 | 0.8 | 55 | 65 | 95 |
|  |  | 24 | 3.0 | 36 | 1.3 | 45 | 55 | 80 |
| 3 | 16# | 16 | 13 | 223 | 0.4 | 50 | 60 | 85 |
|  |  | 18 | 7.5 | 172 | 0.5 | 45 | 55 | 80 |
|  |  | 20 | 7.5 | 89 | 0.7 |  |  |  |
| 4 | 12# | 12 | 23 | 490 | 0.2 | 60 | 70 | 100 |
|  |  | 14 | 17 | 312 | 0.3 | 55 | 65 | 95 |

- Withstanding voltage：Sea level 1500V；30480m 200V（50Hz，AC RMS）

How to order

| Basic series | R97L | 22 |
| --- | --- | --- |
| Contact size | 22、20、16、12 |  |

Outline dimensions

| P/N | Contact size | Amax | B±0.76 |
| --- | --- | --- | --- |
| R97L-22 | 22 | 32.5 | 5.08 |
| R97L -20 | 20 | 36.9 | 6.6 |
| R97L -16 | 16 | 35.6 | 7.62 |
| R97L -12 | 12 | 42.6 | 9.15 |

R97 Series Accessory

Description

- The accessory can achieve straight and right angle entry and EMI shielding for R97 series products

How to order

| Basic series | R97-FJ | A | E | -02 |
| --- | --- | --- | --- | --- |
| Accessory type | A－Shielding B－Non-shielding |  |  |
| Material | E－Stainless steel, passivated F－Aluminum, nickel plating |  |  |
| Length of accessory | 02（Quantity per module） |

When P/N is R97-FJAE-02, J1784A/62-12S is for straight entry and JY599I13FJA90E-10 is for right angle entry

When P/N is R97-FJAF-022, J1784A/62-12N is for straight entry and JY599I13FJA90F-10 is for right angle entry

Outline dimensions

Straight non-shielding accessory

Right angle non-shielding accessory

Shielding accessory

R97-DG1 Series Composite Rail

Description

| 48% lighter than comparable aluminum rails Intermounts with MIL-T-81714 series II rails Operating temperature -65℃~+200℃ Corrosion-proof Allow hand insertion of each individual module. A positive lock retains the module in the rail. Modules can be individually unlocked and removed by using a simple tool Applicable to feedback and distribution modules |  |
| --- | --- |

How to order

| Basic series | R97-DG | 1 | A | -02 |
| --- | --- | --- | --- | --- |
| Material | 1－Composite |  |  |
| Color | A－Black |  |  |
| Length | 02～20 |

Outline dimensions

| P/N | Quantity n | E | F | Module quantity and combination type |
| --- | --- | --- | --- | --- |
| R97-DG1A-02 | 2 | 26.31 | 13.16 | 2+0 |
| R97-DG1A-03 | 3 | 39.47 | 26.31 | 3+0，1+1 |
| R97-DG1A-04 | 4 | 52.63 | 39.47 | 4+0，2+1，0+2 |
| R97-DG1A-05 | 5 | 65.79 | 52.63 | 5+0，3+1，1+2 |
| R97-DG1A-06 | 6 | 78.94 | 65.79 | 6+0，4+1，2+2，0+3 |
| R97-DG1A-07 | 7 | 92.10 | 78.94 | 7+0，5+1，3+2，1+3 |
| R97-DG1A-08 | 8 | 105.26 | 92.10 | 8+0，6+1，4+2，2+3，0+4 |
| R97-DG1A-09 | 9 | 118.41 | 105.26 | 9+0，7+1，5+2，3+3，1+4 |
| R97-DG1A-10 | 10 | 131.57 | 118.41 | 10+0，8+1，6+2，4+3，2+4，1+5 |
| R97-DG1A-11 | 11 | 144.73 | 131.57 | 11+0，9+1，7+2，5+3，3+4，1+5 |
| R97-DG1A-12 | 12 | 157.89 | 144.73 | 12+0，10+1，8+2，6+3，4+4，2+5，0+6 |
| R97-DG1A-13 | 13 | 171.04 | 157.89 | 13+0，11+1，9+2，7+3，5+4，3+5，1+6 |
| R97-DG1A-14 | 14 | 184.20 | 171.04 | 14+0，12+1，10+2，8+3，6+4，4+5，2+6，0+7 |
| R97-DG1A-15 | 15 | 197.36 | 184.20 | 15+0，13+1，11+2，9+3，7+4，5+5，3+6，1+7 |
| R97-DG1A-16 | 16 | 210.52 | 197.36 | 16+0，14+1，12+2，10+3，8+4，6+5，4+6，2+7，0+8 |
| R97-DG1A-17 | 17 | 223.67 | 210.52 | 17+0，15+1，13+2，11+3，9+4，7+5，5+6，3+7，1+8 |
| R97-DG1A-18 | 18 | 236.83 | 223.67 | 18+0，16+1，14+2，12+3，10+4，8+5，6+6，4+7，2+8，0+9 |
| R97-DG1A-19 | 19 | 249.99 | 236.83 | 19+0，17+1，15+2，13+3，11+4，9+5，7+6，5+7，3+8，1+9 |
| R97-DG1A-20 | 20 | 263.14 | 249.99 | 20+0，18+1，16+2，14+3，12+4，10+5，8+6，6+7，4+8，2+9，0+10 |

注：① Figure behind “+” designates the quantity of the module with single width，Figure behind “+” designates the quantity of the module with dual width. “5+2” designate 5 modules with single width and 2 modules with dual width

②During mounting the rail, the locking bolt are evenly distributed to ensure the even stress

R97-DG2 Single Module Metal Rail

Description

| The rail is made from aluminum alloy and accepts one module with single width or 2 modules with single width. It is black anodized, cadmium and nickel plated. When it is clear cadmium plated, the temperature is limited to below 125℃ |  |
| --- | --- |

How to order

| Basic series | R97-DG | 2 | A |
| --- | --- | --- | --- |
| Code | 2－Single module metal rail |  |
| Finish | A－Black anodized B－Olive drab cadmium C－Clear cadmium D－Nickel plating |  |

Outline dimensions

R97 Series Tool

Tool for crimped socket

| Contact size | Insertion/ removal tool | Crimping tool | Locator | Sealing plug |
| --- | --- | --- | --- | --- |
| 22# | M81969/14-01 | YJQ-02 | XDWQ-20 | 21E8-336-018-P4（Black） |
| 20# | M81969/14-10 | YJQ-02 | XDWQ-21 | 21E8-336-019-A1（Red） |
| 16# | M81969/14-03 | XCXY-02 | DWQ-36 | 21E8-336-020-P7（Blue） |
| 12# | M81969/14-04 | XCXY-02 | DWQ-36 | 21E8-336-021-A1（Yellow） |
| 10# | M81969/14-05 | XCXY-01 | DWQ-32 | 21E8-336-030-P50（White） |

Note：1）Sealing plug is installed on non-used cavity；2）Crimping, locator and sealing plug should be ordered separately

Module Removal tool

|  | Assembly procedure as shown： |  |
| --- | --- | --- |
|  | Step 1 | Step 2 |
|  | Step 3 | Step 4 |

Annex: Composite Termination Module Crimp Operation Instruction and Notes

Crimp procedure

Step 1：Strip the wire

Step 2：The core exceed the inspection hole of barrel

Step 3：Place the contact in the crimping tool

Step 4：Insert the wire into barrel

Step 5：Squeeze the handle to the closed position

Step 6： Remove the hand

Step 7： The handle is released automatically

Step 8： Remove contact

Inspection the crimping quality

After crimping the contact, the crimp quality should be inspected. For the following items, 3 crimped parts should be prepared before manufacturing and will be conducted the crimped strength and crimped resistance inspection. The parameters should be in accordance with contact resistance, rated current, pull and crimped resistance table.

- Before using the new crimping tool

- Before a batch of crimping are used

- After crimping every 5000 parts

- Doubt on the crimped quality

Examine the following items：

1、Appearance

- The crimping point examination：

The crimping point should be even and the crimped parts should not bend. The core should be inserted into the barrel and be visual with the inspection hole；

- Crack inspection：

Inspect the crimped parts with ten magnification. No cracks on the basic metal due to crimped ；

- The indentation and the length of exposed core：

Examine the axial position and the length of exposed core with the calipers. The axial position and the length of exposed length should not be more than 0.8mm（see figure 1）

| Figure 1 | Figure 2 |
| --- | --- |

2 Examine the crimped resistance

According to contact P/N and wire size, determine the maximum contact resistance R according to contact resistance, rated current, pull and crimped resistance table. Measure contact resistance according to the position in figure 2 （Add the stripped length for measurement to 5~8mm）, the measured result should be less than R。

3、Examine the crimped strength

According to contact P/N and wire size, determine the minimum tensile strength F according to table contact resistance, rated current, pull and crimped resistance. Crimped contacts as shown in the following figure and measure the tensile strength which should be more than the specified value in contact resistance, rated current, pull and crimped resistance table.

Figure 3

Notes

- Cross section of wire should be matchable with the contact；

- No broken wire and damage during stripping；

- The core should exceed the inspection hole of barrel；

- No under-crimp or over-crimp；

- If the crimping is not in place, the crimping tool is squeezed to the required place,。

R97，J20 Series Electrical Modules

Description

- In accordance with HB6384

- Refer to the structure of France NF-C93462

- Connecting module with 20#, 16# contacts

- Adapting module R97﹠grounding module J20

- Crimped contact

- Various circuit array

- Silicone and thermosetting resin as insulator

- Enterprise standard：21E0.204.018

Main technical characteristic

| [Mechanical] | [Environmental] |
| --- | --- |
| Vibration：5～500Hz，Acceleration 140m/s2 Shock：Acceleration 200m/s2 Constant acceleration：150m/s2 | Temperature: Level I：-55～+200℃ Level Ⅱ: -55～+125℃ Relative humidity：95% at 40℃ |
| []Electrical] |  |
| Insulation resistance：normal≥5000MΩ，heat﹠damp ≥100MΩ Contact resistance and rated current： Contact size Contact resistance（Ω） Rated current（A） # 16 ≤0.0015 13 # 20 ≤0.0025 7.5 | Rated voltage：115V Withstanding voltage： Operation environment Withstanding voltage（V） （50HzAC RMS） Duration（min） 101.3kPa 1500 1 1kPa 300 Heat＆damp 1125 |

How to order

[R97 series adapting module]

| Basic series | R97 | A | 20 | -01 | -Ⅰ |
| --- | --- | --- | --- | --- | --- |
| Cavity marking | A－without marking；B－with marking |  |  |  |
| Contact size | 20、16 |  |  |  |
| Insert arrangement | See insert arrangement |  |
| Temperature level | Ⅰ－Ⅰlevel -55～+200℃；Without marking－Ⅱlevel -55～+125℃ |  |

[J20 series grounding module]

| Basic series | J20 | -16 | -Ⅰ |
| --- | --- | --- | --- |
| Contact size | 20、16 |  |
| Temperature level | Ⅰ－Ⅰlevel -55～+200℃；Without marking－Ⅱleve -55～+125℃ |  |

Outline dimension and insert arrangement

[20号contact module]

| 20# adapting module （R9720－） | 20# grounding module （J20－20） |
| --- | --- |

[20# contact insert arrangement]

| R97B20-adapting module Insert arrangement with marking | R97A20- adapting module Insert arrangement without marking |
| --- | --- |

[16# contact module]

| 16# adapting module （R9716－） | 16# grounding module （J20－16） |
| --- | --- |

[16# contact insert arrangement]

| R97B16--adapting module Insert arrangement with marking | R97A16- adapting module Insert arrangement without marking |
| --- | --- |

Accessory

[Contact, wire and crimping tool]

|  | Contact |
| --- | --- |
|  | Contact size | A | B | C | D |
|  | 20# | 7.5 | 4.3 | 2 | 1.3 |
|  | 16# | 9.8 | 6 | 2.6 | 1.7 |
| Applicable wire and crimping tool |
| 接触件号Contact size | I.D. of barrel mm | O.D. of barrel mm | Cross section (mm2) | Wire gauge （AWG） | Crimping tool | Locator | International crimping tool |
| 20# | 1.3 | 2 | 0.21～0.93 | 18、20、22、24 | YJQ-02 | XDWQ-15 | M22520/1-01 |
| 16# | 1.7 | 2.64 | 0.60～1.34 | 16、18、20 | XCXY-01 | DWQ-52 |  |

[J23 pressure module]

[Sealing plug]

The accessory is used for sealing the stand-by contact. Sealing plug can prevent dust, rain and so on.

|  | Size | d | D |
| --- | --- | --- | --- |
|  | 20 # | 2.2 | 3.5 |
|  | 16 # | 2.6 | 4 |

JZ Series Relay Receptacle

Description

| JZ series connectors are widely used in aviation, space and ship and are straight mating relay receptacles with lug mounting. Its technical performance is in accordance with MIL-S-12883 Enterprise standard：21E0.204.033JT |  |
| --- | --- |

Main technical characteristic

——Operating temperature：-55℃～+125℃

——Relative humidity：95% at 40±2℃

——Vibration：Vibration 10～2000Hz，Acceleration 200m/s2

——Durability：500 cycles

——Altitude：24000m

——Rated voltage：DC 28V，AC 115V/200V

——Insulation resistance：norma≥2000MΩ  heat﹠damp≥50MΩ

——Contact resistance and rated current：

| Contact size | 22#（Φ0.76） | 20#（Φ1.0） | 16#（Φ1.6） | 12#（Φ2.4） |
| --- | --- | --- | --- | --- |
| Contact resistance （Ω） | ≤0.010 | ≤0.007 | ≤0.004 | ≤0.002 |
| Rated current（A） | 3 | 5 | 10 | 35 |

How to order

| Basic series | JZ－Relay receptacle | JZ | 001 | -08 | Y |
| --- | --- | --- | --- | --- | --- |
| Applicable relay serial number | 001、210、215、220、300、400、500、550 |  |  |  |
| Number of contact | 05、08、11、14 |  |  |
| Mounting style | Y－Crimped |

* See outline dimensions for specific P/N

Insert arrangement

Outline dimensions

| Figure 1 | Figure 2 | Figure 3 |
| --- | --- | --- |
| Figure 4 | Figure 5 |  |

| P/N | Contact size | Quantity | A | B | C | D | E | F | G | H | J | Figure |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| JZ001-08Y | 20# | 8 | 34.1 | 27 | 10.5 | 19 | 27.3 | 5.08 | 5.08 | 6 | — | Figure 1 |
| JZ210-08Y | 20# | 8 | 36 | 27.3 | 10 | 20 | 17 | 3.81 | 3.81 | 4.7 | 1.9 | Figure 2 |
| JZ300-08Y | 16# | 8 | 43 | 35.7 | 13 | 25 | 21 | 5.08 | 5.08 | 5.6 | 2.54 |  |
| JZ220-14Y | 20# | 14 | 36 | 27.3 | 20 | 20 | 17 | 3.81 | 3.81 | 4.7 | 12.7 | Figure 3 |
| JZ400-14Y | 16# | 14 | 43 | 35.7 | 25 | 25 | 21 | 5.08 | 5.08 | 5.6 | 15.9 |  |
| JZ500-11Y | 12# 16# | 9 2 | 43 | 35.7 | 25 | 25 | 21 | 5.94 | 7.62 | 5.6 | 15.9 | Figure 4 |
| JZ550-11Y | 12# 16# | 6 5 | 43 | 35.7 | 25 | 25 | 21 | 5.94 | 7.62 | 5.6 | 15.9 |  |
| JZ215-05Y | 20# 16# | 2 3 | 32.6 | 27.2 | 10 | 20.6 | 21 | 5.08 | 5.24 | 5.6 | 2.54 | Figure 5 |

Receptacle mounting style

| Mounting style Ⅰ （Only applicable to JZ001-08Y） | Mounting style Ⅱ （Only applicable to JZ001-08Y） | Mounting style Ⅲ （for JZ210-08Y） |
| --- | --- | --- |
| Mounting style IV |  |  |

Applicable wire and tool

| Contact size | 20# | 16# | 12# |
| --- | --- | --- | --- |
| Diameter of contact | Φ1.06 | Φ1.6 | Φ2.4 |
| Wire gauge | 24、22、20 | 20、18、16 | 14、12 |
| Crimping tool | YJQ-02 | XCXY-02 | M22520/1-01 |
| Locator | M22520/7-12 | For JZ001-08Y JZ210-08Y JZ220-14Y | M22520/7-13 | For JZ215-05Y | DWQ-42 |
|  | XDWQ-19 | For JZ215-05Y | DWQ-41 | For JZ300-08Y JZ400-14Y JZ550-11Y |  |
| Removal tool | QG-001 SG-001 | M81969/14-03 | M81969/14-04 M81969/10-03 |